## Slide 1
Multilane Racetrack Caches: Improving Efficiency Through Compression and Independent Shifting
Published in:
Design Automation Conference (ASP-DAC), 2015 20th Asia and South Pacific
08/26/2015

## Slide 2: Outline for Today’s Presentation
introduction to Racetrack memory (RM)
multilane Racetrack caches (MRC) design
  fundamental structure
  in-place compression
  independent shifting
  skewed alignment
experimental methodology
results
conclusion

## Slide 3: Introduction To Racetrack Memory (RM)
also referred to as domain-wall memory, extension to STT-MRAM
bits in RM are stored on magnetic nanowires (or tracks) separated by domain walls
access points similar to a magnetic tunnel junction (MTJ) for reads/writes to the aligned domain
by applying spin-polarized current pulses, data bits can be shifted along the track to be aligned with these access points
multi-port-on-one-track (MP1T)
one-port-on-one-track (1P1T)
3D, larger storage density,
achieves 5% performance gain, and 19% energy reduction

## Slide 4: Bit-interleaved Mapping Of TapeCache
one-port-on-one-track (1P1T) is the smallest repeating unit in RM which can store tens to hundreds of bits
  all of them share the same access port
to avoid port contention within a single access, bit-interleaved mapping of TapeCache is adopted
figure shows Bit-interleaved data array organization
  all the tape heads move in a lock step fashion

## Slide 5: MRC LLC Design – Fundamental Structure
figure illustrates the logical view of a RM cache “data sub-array”
vertical lines represent cache lines, while horizontal lines of the data sub-array are physical tracks
1KB sub-array
2-way set-associative
64-byte block size
16-cache lines (16-bit Racetrack)
1-byte has 8 tracks
512 tracks

## Slide 6: MRC LLC Design – In-place Compression
normally cache compression schemes attempt to increase effective cache capacity
here compression is used to save read, write, and shift energy while accelerating accesses to the RM LLC
a compressed cache line has fewer bits to write than the uncompressed line, and thus requires less energy to write and read
compression and decompression require energy overheads
  lightweight compression methods including ZERO, Repeated Values, and BDI are used over complicated ones

## Slide 7: Compression Schemes
zero: applies when the data is zero
Repeated Values: if the data repeats every x bytes then it can be compressed by the REPx scheme
BDI: if we divide a cache line into y-byte sub-blocks and all offsets between the first sub-block with each of the remaining sub-blocks being within a z-byte range, then the line is compressible by the ByDz (y-byte base, z-byte delta) scheme
B4D2 Scheme

## Slide 8: 14 Effective Compression Schemes
initially, 14 effective compression schemes were evaluated from in-place compression
  14 compression schemes (including uncompressed) ordered by sizes after compressing a 64 byte cache line
each compression/decompression scheme requires additional hardware and energy overhead
by observing above table we can say that several schemes have similar compressed sizes

## Slide 9: Comparison Between 14 Compression Schemes
below graph shows the breakdown of occurrences of 14 compression schemes (including uncompressed) in 5 applications with small input sets
the graph indicates that several schemes are rarely applied
four dominating compression schemes (ZERO, REP4, REP8, B4D2) are selected to go with uncompressed data

## Slide 10: MRC LLC Design – Independent Shifting
ZERO, REP4, REP8, B4D2, and uncompressed scheme are selected among 14 schemes
  a cache line can require 0, 4, 8, 34, and 64 bytes for each of the compression scheme respectively
thus authors propose to independently shift every 16 tracks or 2 bytes (the greatest common divisor of the 4 non-zero sizes) instead of shifting the whole block
  for example, in order to access a cache line compressed by the REP4 scheme, we only need to shift 32 tracks or 4 bytes (we do not need to shift remaining 480 tracks or 60 bytes) to be aligned with the access ports to read the cache line
considerable shift energy can be saved in this way through compression combined with independent shifting

## Slide 11: MRC LLC Design – Skewed Alignment
in-place compression and independent shifting are effective to save dynamic power but do not provide a performance improvement
as compressed cache lines reduce the bits to be written, it is not necessary to align them with the beginning of the storage cell
in TapeCache, two accesses must stall until one finishes as all the bits on the same track share a single port
after each access completes, the tracks must be shifted by at least two domains to allow the next cache line to be accessed at the port
due to the spatial locality of access present in many applications, the contention may occur while accessing the bit
this contention turns out to be very common and can result in significant performance degradation

## Slide 12: MRC LLC Design – Skewed Alignment Example
in the scenario given below, if data align at beginning of the cache line for W0 in first 3 sets, contention may occur
if the three cache lines can be compressed into the sizes of the shaded bars as shown in figure and their alignment skewed accordingly by leveraging independent shifting
  sub-array contention is reduced and both energy and performance improvement can be achieved

## Slide 13: MRC LLC Design And Operation
compression
independent shifting
skewed alignment

## Slide 14: Experimental Methodology/Setup
extended the Sniper full system simulator to include a Racetrack LLC structure
for latency, power, and area parameters
  used CACTI to model SRAM, NVSim to model STT-MRAM, and modified NVSim to model RM
used 20 parallel applications drawn from the Parsec and Rodinia benchmark suites for simulation workloads
below table shows global architecture parameters used

## Slide 15: LLC Parameters Of Different Memory Technologies

## Slide 16: Performance Comparison Of 6 LLC Schemes
MRC is able to improve the performance of Racetrack memory by more than 5% for both MRC-16 and MRC-32
the performance improves by 4% and 3.5% for 16-bit and 32-bit tracks, respectively, over SRAM
in some applications, such as dedup and pathfinder, we observe dramatic (i.e., over 10%) IPC improvements for MRC-16 and MRC-32 from the high compression ratios
MRC degrades performance in raytrace and srad because the compression/decompression overheads yield relatively low compression rations

## Slide 17: Energy Consumption Comparison Of 6 LLC Schemes
non-volatility helps STT-MRAM and RM to achieve significant energy savings compared to SRAM: 7.68x on average
both MRC-16 and MRC-32 have 19% more energy savings compared to RM-16 and RM-32 respectively

## Slide 18: Energy breakdown of a 1MB Racetrack
below figure represents the break down of the LLC energy consumption of the MRC-16 scheme into five parts
the static energy consumed by the SRAM tag array and other peripheral circuitry accounts for 51.5% of the total consumption
reads, writes take up 20.2% and 8.5% respectively, shift operations consume 18.3%, and lightweight compression/decompression consumes only 1.5% of the remaining energy

## Slide 19: Conclusion
pros:
  MRC allows cache lines mapped to the same Racetrack structure to be accessed in parallel when compressed, mitigating potential shifting stalls in the RM cache
  MRC improves performance by 5% and reduces energy by 19% compared to an isocapacity baseline RM cache resulting in an energy delay product improvement of 25%
cons:
  shifting overload caused by shift controller is not considered in skewed alignment
    shifting consume a lot of energy
  though the MRC reduces energy consumption, performance improvement is not significant
    it is not consistent and varies according to different applications/benchmarks

## Slide 20
  Thank You
  Questions?

## Slide 21
  My Current Work

## Slide 22: STTRAM and Racetrack LLC in GPUs
modeled STTRAM and Racetrack LLC area/size parameters using GPGPUsim
  replaced traditional SRAM L2 cache area/size parameters with STTRAM and Racetrack parameters
  GPU used : NVIDIA GTX480 for simulation
  benchmarks used : ISPASS-2009
made changes in the configuration
  size of SRAM ~ 4 x size of STTRAM ~ 4 x size of Racetrack
compared L2 cache average dynamic power and GPU total average power for all memories
next steps : looking to modify other parameters that affects LLC power

## Slide 23: L2 Cache Average Dynamic Power

## Slide 24: GPU Total Average Power